## Slide 1
Sugon Disk System DS600-G20 Overview
Storage Product Department

## Slide 2
Contents
1
DS600-G20 Overview
2
DS600-G20 Administration Configuration
3
DS600-G20 Maintenance
4
DS600-G20 FAQ
Notes: 先讲整个IT行业的大背景

## Slide 3
NAS function
CIFS (MAC, Windows), NFS (Linux/Unix) Protcol
Permission Management, Quota Management, Online Expansion
MANAGEMENT & OPERATION
Power button and power resume management
PerfectFlash™ -Non-disruptive image update without system downtime
Built-in performance monitor and power usage monitoring
OPAS Service Log and UPS Monitor through USB
Support Wake-on-LAN and Wake-on-SAS
Mute alarm control
Product Features and Highlights
SYSTEM & CONTROLLER
64bit 6-core @ 1.1GHz Processor
Standard 2GB cache per controller (up to 16GB)
Fiber Channel 8Gbps, iSCSI 1Gbps & 10Gbps host connect ports
Dual Controller High Availability Design
High Scalability (112 HDDs) and Green Design
DATA PROTECTION
Predictive Data Migration (PDM)
PerfectRebuild - Rebuild with improved recovery efficiency
Advanced battery flash backup
Online LUN clone (available in SR1)
Hard disks cache backup (available in SR3)
Notes: 先讲整个IT行业的大背景

## Slide 4
Product Specifications
Technology Specifications | DS600-G20 (Single Controller) |  | DS600-G20(Dual Controller)
Controller | Hot swap, single controller |  | Hot swap, dual redundant controller, Active-Active mode
Processor | 64-bit Multi-core processor |  | 
Cache | 2GB-16GB | 4GB-32GB | 
Cache Battery Protection | Lithium Battery |  | 
Flash Cache Protective Film Group | Standard configuration of permanent Cache-backup unit, no limitation for power-off time |  | 
Host Channel for Controller | 4x 1Gb ISCSI host interface, addition of 2x 10Gb ISCSI host interface and2x 8Gb FC host port available |  | 
Disk Channel | 4x SAS Disk Expansion Interface |  | 
RAID Level | 0, 1, 1E, 3, 5, 6, 10 (0+1), 30, 50, 60 |  | 
Hot Spare | Overall and part hot standby supported, auto rebuild in RIAD backstage |  | 
Support Block Protocol | ISCSI, FC |  | 
Support File Protocol | SMB/CIFS, NFS, AFP, FTP, WebDAV |  | 
Support Share Disk | Authority management, Quota management, Online capacity expansion |  | 
Physical Characters |  |  | 
Maximum of Disk | Up to connect 6x JBOD, up to 112x disks |  | 
Disk Size Supported | 2TB, 3TB, 4TB(7200 RPM) 3.5” SATA / NL SAS, 600GB(15K RPM) 3.5” SAS, 120GB, 240GB, 480GB 2.5” SSD |  | 
Dimension | Standard 3U height 19 in rack(131x447x507mm) |  | 
Power, Fan | 2+1 redundant power, edundant fans, support online exchange |  | 
Net Weight | 20.1kg (no disk) |  | 
Noise | 55dB -75dB |  | 
Management Characters |  |  | 
Management Interface | Sugon RAID Management Software |  | 
Fault Alarm | Interface Alarm, sound-light alarm, E-mail alarm, SNMP |  | 
Logging | Real-time display of alarm logging, import and export, etc. supported |  | 
System Compatibility |  |  | 
Fiber Equipment Supported | LSI, Qlogic, Emulex, Brocade, etc. |  | 
OS Supported | Windows Server 2003/2008, Red Hat Linux 5.X/6.X, SUSE Linux Enterprise Server 10.X/11.X，Vmware ESX, etc. supported |  | 
Notes: 先讲整个IT行业的大背景

## Slide 5
Front Panel Light
Controller Light
Extended Cabinet
Light
Component Light
  Power Module
  Fan Module
  BBU Battery
LED Indicator
Power
OPAS Status Light
OPAS Interface
Mute Light
Mute Button
Power Light
Disk Cabinet Status Light
RAID Status Light
Controller 1 Status Light
Controller 2 Status Light
System Status Light
Disk Status Light
Power Status Light
Extended Cabinet Status Light
SAS Extended OUT Port
Status Light
SAS Extended IN Port
Status Light
Controller Status Light
SAS Extended Port Light
Dirty Data
Status Light
Host I/O 1 Status Light
Host I/O 2 Status Light
Port Management
Status Light
Zhongke Sugon
Notes: 先讲整个IT行业的大背景

## Slide 6
Front panel LED Lights
电源
机箱状态灯
RAID状态灯
控制器状态灯.
系统状态灯
控制器心跳灯
智能开关
硬盘电源
硬盘状态
智能管理口
静音
Disk Power
Power
Disk Status
Intelligent
Switch
Mute
Intelligent Management Port
Case Status Light
RAID Status Light
Controller Status Light
System Status Light
Controller Heartbeat Light
Notes: 先讲整个IT行业的大背景

## Slide 7
Controller LED Lights
LED Indicator | Instruction
SAS Extended Port Status Light | Green：Link Extended Cabinet
Port Management Status Light | LED light on the left shows that if there is connection： Off：no connection；Green：connect LED light on the right indicates port rate： Green：100Mbps
Controller Status Light | Green：Controller works
Dirty Cache Status Light | Amber：Dirty Data exist in the controller cache which is still not freshed into the disk Off：No Dirty Data
Controller Status Light
SAS Extended Port Light
Dirty Data
Status Light
Host I/O 1 Status Light
Host I/O 2 Status Light
Port Management
Status Light
Notes: 先讲整个IT行业的大背景

## Slide 8
Host I/O of DS600-G20 includes 1Gb ISCSI、10Gb iSCSI、8Gb FC
Controller LED indicators
LED Light | Instruction
1Gb ISCSI Port Status Light | LED Light on the left shows if there is connection： Off：no connected；Green：connected LED light on the right indicates ISCSI port rate： Amber：1000Mbps；Green：100Mbps
10Gb ISCSI Port Status Light | LED Light on the left shows if there is connection： Off：no connected；Green：connected LED light on the right indicates ISCSI port rate： Amber：10000Mbps；Green：1000Mbps
FC Port Status Light | Single LED light shows connection status and port rate via green and amber Green flashes slowly and amber flash at 4Hz indicate that connection is normal and rate is 8Gbps Green off：port abnormal
Notes: 先讲整个IT行业的大背景

## Slide 9
Component LED Lights
Power indicator
  Green：Normal
  Red：Power abnormal or component false
Fan indicator
  Green：Normal
  Red： component failure
BBU indicator
  Green：Normal, full scale of energy
  Amber ： on charge
  Red：no battery or battery failure
Notes: 先讲整个IT行业的大背景

## Slide 10
TopologicalLink
Notes: 先讲整个IT行业的大背景

## Slide 11
Boot of storage system
  Press the button on the front panel to start up, after the extension cabinet is connected, the main cabinet switch button to achieve the storage system of the switch machine.
Shutdown of storage system
  Shutdown requires a long press switch button 5s, after the red indicator lights, the system will automatically save the data off the storage system.。
  In the web management interface to close the storage
Order of boot and shutdown
Switch Power
Disk array host boot
Network equipment, server boot
Server boot is generally in the last.
Stop I/O. empty cache
Turn off the server (after emptying Cache)
Turn off the disk array host
Notes: 先讲整个IT行业的大背景

## Slide 12
Contents
1
DS600-G20 Overview
2
DS600-G20 Administration Configuration
3
DS600-G20 Maintenance
4
DS600-G20 FAQ
Notes: 先讲整个IT行业的大背景

## Slide 13
Web management interface
  Browser access
  Default management IP 10.0.0.1
CLI command line interface
  Serial port, Telnet, SSH access
CLU command tool
  Serial port, Telnet, SSH access
DS600-G20 management software
Notes: 先讲整个IT行业的大背景

## Slide 14
Serial type RJ11-DB9
Serial port parameter
  Baud rate ：115200
  Data bits ：8
  Stop bit ：1
  Parity check: no
  Flow control: no
Username :administrator
Password :password
Common operations
  View / modify management IP
Serial Login
Enter menu
Management IP settings
Notes: 先讲整个IT行业的大背景

## Slide 15
Web management software
Based on WEB management tool, compatible with mainstream browser
Chinese management configuration interface
Full graphical interface
The use of a built-in efficiency, performance monitoring management center
The default IP address ：10.0.0.1
Username ：administrator
Password：password
Notes: 先讲整个IT行业的大背景

## Slide 16
Web management software main interface
Notes: 先讲整个IT行业的大背景

## Slide 17
Serial number | Name | Introductions
① | Login status display | Display the current IP address and the logged in user
② | Main function selection | Management software system, NAS two part feature set, [System] is mainly to provide a block device (DAS, SAN) disk array configuration and management capabilities overall monitoring [NAS] provides NAS management feature set, through button to switch to different functional configuration area .
③ | Navigation bar | [System] and [NAS] interface, each containing a number of configuration modules. [System] screen contains the [Dashboard], [Device], [Storage], [Administration] module; [NAS] interface contains [Dashboard], [File System], [Account], [Misc] module
④ | Display and configuration area | Display detailed information about navigation bar of each module, and provide configuration capabilities
⑤ | Service & Help | Including [Save Service Report], [Help], [Contac Us], [About], [Logout] button, etc.
⑥ | Discovery | Automatic discovery and automatically jump to the same management segment other storage devices
Web management software main interface
Notes: 先讲整个IT行业的大背景

## Slide 18
iSCSI Configuration Process
Notes: 先讲整个IT行业的大背景

## Slide 19
ISCSI network and software configuration
  Create iSCSI entry
  The application server is configured to keep the network connected to the iSCSI portal.
  Application server to start iSCSI
    Windows OS：iSCSI initiating program
    Linux OS： iscsi or open-iscsi package
iSCSI Configuration
Notes: 先讲整个IT行业的大背景

## Slide 20
Create a storage space - create a disk array (DA)
iSCSI Configuration
Notes: 先讲整个IT行业的大背景

## Slide 21
Create a storage space - create a logical disk (LD)
iSCSI Configuration
Notes: 先讲整个IT行业的大背景

## Slide 22
Establish a connection to the iSCSI configuration starter - add target portal
iSCSI Configuration
Notes: 先讲整个IT行业的大背景

## Slide 23
Establish a connection to the iSCSI configuration to connect host starter - (Linux)
iscsiadm -m discovery -p 10.0.30.1 -t st
  iscsiadm -m node -p 10.0.30.1 -l
iSCSI Configuration
Notes: 先讲整个IT行业的大背景

## Slide 24
Establish a connection to the iSCSI - add a starter
iSCSI Configuration
Notes: 先讲整个IT行业的大背景

## Slide 25
Establish iSCSI connection -LUN map
iSCSI Configuration
Notes: 先讲整个IT行业的大背景

## Slide 26
Application server to identify storage space
iSCSI Configuration
Notes: 先讲整个IT行业的大背景

## Slide 27
FC Configuration Process
End
Start
Yes
No
LUN mapping
Identify storage space
LUN masking
Configuration starter
Application server storage space
Create logical disk
Create disk array
Establish a connection
Create storage space
FC link configuration
FC link configuration
Notes: 先讲整个IT行业的大背景

## Slide 28
FC Link Configuration
  The application server FC HBA cards and FC disk array connected to the port, which can be directly connected or connected to FC switch connected after checking each FC port light is on.
Create storage space (see iSCSI configuration)
  Create Disk Array （DA）
  Create logical disks （LD）
Configure the FC starter
FC Configuration
Notes: 先讲整个IT行业的大背景

## Slide 29
LUN mapping
FC Configuration
Notes: 先讲整个IT行业的大背景

## Slide 30
Multipath Management Software
  Windows Application Server ：Multipath Manager-[version] software
  Linux Application Server ： The system comes with device-mapping-multipath software
Path redundancy strategy
  Windows Application Server
  Linux Application Server
iSCSI/FC Multipath
Or multi bus
Or round robin
Notes: 先讲整个IT行业的大背景

## Slide 31
NAS Configuration Process
Notes: 先讲整个IT行业的大背景

## Slide 32
NAS Network Configuration
NAS Configuration
Notes: 先讲整个IT行业的大背景

## Slide 33
Creating a shared directory - creating a disk pool
NAS Configuration
Notes: 先讲整个IT行业的大背景

## Slide 34
Creating a shared directory - creating a shared disk
NAS Configuration
Notes: 先讲整个IT行业的大背景

## Slide 35
User Authentication - Local Users
NAS Configuration
Notes: 先讲整个IT行业的大背景

## Slide 36
User Authentication - Domain User
NAS Configuration
Notes: 先讲整个IT行业的大背景

## Slide 37
Setting quotas
NAS Configuration
Notes: 先讲整个IT行业的大背景

## Slide 38
CHMOD
NAS Configuration
Notes: 先讲整个IT行业的大背景

## Slide 39
NAS protocol access
  CIFS
  NFS
NAS Configuration
Notes: 先讲整个IT行业的大背景

## Slide 40
Contents
1
DS600-G20 Overview
2
DS600-G20 Administration Configuration
3
DS600-G20 Maintenance
4
DS600-G20 FAQ
Notes: 先讲整个IT行业的大背景

## Slide 41
Event Management
Level | Introductions
Fatal | There is an error in the system.
Critical | There is a serious problem that needs to be dealt with as soon as possible.
Major | Need to take some measures.
Minor | There are some problems, and some suggestions are proposed.
Warning | Users decide whether to take measures.
Information | System information, without taking any measures.
Notes: 先讲整个IT行业的大背景

## Slide 42
Ways of finding fault
  Buzzer alarm sound;
  All kinds of LED lights;
  Regularly check [event management] in the event record, if the management of the user to enable the event notification, in accordance with the rules of the event will be notified in the form of e-mail users;
  SNMP monitoring;
  Application server business exception, etc.
Troubleshooting recommendations
  Check the various types of LED lights;
  To see if there are Fatal, Critical, Minor, Major, etc.
System Troubleshooting
Notes: 先讲整个IT行业的大背景

## Slide 43
Service reports are used to analyze the underlying problems of the storage system, which can be used to export the service report in two ways when the failure is encountered.
  Method 1 In the web administration interface, click [Save Service Report], the XX.zip saved locally.
  Method 2 U flash disk is inserted into the OPAS interface of the front panel of the main cabinet, waiting for a few minutes, the service report will be automatically saved to the U flash disk.
Service report export
Notes: 先讲整个IT行业的大背景

## Slide 44
Contents
1
DS600-G20 Overview
2
DS600-G20 Administration Configuration
3
DS600-G20 Maintenance
4
DS600-G20 FAQ
Notes: 先讲整个IT行业的大背景

## Slide 45
After adding the AD domain, MAC OSis unable to access the SMB directory with the local user.
  After adding the AD domain, OS MAC will be automatically added to the user name DOMIAN information, that is, the local user will become the form of DOMAI／username, and therefore can not be accessed by local users SMB.
LDAP domain server management
  After adding the LDAP domain，
  Local users can not be used, when the exit of the LDAP domain after the local users to continue to use；
  Local users can not modify, add and delete；
  Before setting the quota and permissions for local users will be cleared；
  The user uid of the proposed LDAP server starts from 1000.
FAQ
Notes: 先讲整个IT行业的大背景

## Slide 46
Maximum capacity of shared disk
  The maximum capacity shared by the shared disk is related to the memory capacity of the controller.
Name limit for disk pool and shared disk
  Not allowed to contain the following characters ：
  .`~!@#$%^&*()+={}[]|\:;"'<>,?/ and blanks
FAQ
Controller memory capacity | Shared disk allows maximum capacity
2GB | 8TB
4GB | 16TB
8GB | 32TB
16GB | 100TB
Notes: 先讲整个IT行业的大背景

## Slide 47
Local user /User group name restriction
  The following characters are not allowed；
  The maximum length is 30 bytes；
  Can‘t be empty；
  Reserved local users ："root", "daemon", "sshd", "nobody", "messagebus" and "administrator“
  Reserved local user group： "root", "bin", "daemon", "sys", "adm", "tty", "disk", "mem", "kmem", "wheel", "uucp", "utmp", "rpcuser", "rpc", ntp", "ftp", "nobody", "users" ,"administrator“
Local user password restrictions
  Allows a minimum number of characters to be 6, and the maximum number of characters is 16, and does not allow 'symbol and double byte characters (such as Chinese, etc.).
FAQ
Notes: 先讲整个IT行业的大背景

## Slide 48
Whether can through the management port access to a Shared directory
  Port management can be accessed through the shared directory, but if necessary, please use the data access port as soon as possible.
NFS mount directory
  Mount directory is / FS / [share Disk Name], when that is in the shared directory must be mounted before the plus / FS /.
In the Windows operating system, how to clear the temporary log information for Samba users?
  Enter under cmd：net use /delete *
  Wait about 10s of time to re-login.
FAQ
Notes: 先讲整个IT行业的大背景