## Slide 1: Product Introduction of Sugon S640-G20
Storage product division

## Slide 2
Contents
1
The Introduction of Storage Server Market
2
Introduction of S640-G20 product
3
Introduction of S640-G20 product features
4
Product competitive analysis of S640-G20
Notes: 先讲整个IT行业的大背景

## Slide 3
The market of storage server
Large amount of data (PB);storing data online or nearly line;need large storage capacity
Data usually needs to be processed, having certain requirements for computing capacity of the system
For not high requirements of data reliability, the data can be obtained or multi-copies
Need to improve server room installed density and lower overall TCO users

## Slide 4
The analysis of storage server for industry application
互联网云盘
视频网站存储节点
共有云盘运营支撑平台
视频网站，IPTV
视频推流服务器
内容分发服务器
高密度存储节点
云存储高密度节点
定制化软、硬一体集成设备
高端NVR服务器
备份一体机
大数据高密度节点
The Internet Cloud disk
Video websites storage Node
Shared cloud disk operation support platform
Video Websites, IPTV
Video flow server
Content delivery serve
High Density Storage Nodes
Cloud storage high density Nodes
Big data high density Nodes
Customized Soft /Hard Integration Equipment
High-end NVR Server
ESTOR

## Slide 5
Contents
1
The Introduction of Storage Server Market
2
Introduction of S640-G20 product
3
Introduction of S640-G20 product features
4
Product competitive analysis of S640-G20
Notes: 先讲整个IT行业的大背景

## Slide 6
Product Introduction of S640-G20
Standard | Description
Storage Capacity | Maximum 216TB Supporting maximum 24/36pcs 3.5inch hard disk + 4pcs 2.5 inch hard disk
Processor | Two way Intel Xeon E5-2600 v3 series
Chipset | Intel C610
Memory | 24 pcs DIMM slot, support maximum 1.5 TB cache
Network Controller | Two I350 gigabit Ethernet port
Store Controller | 12Gbps SAS controller or 12Gbps SAS Raid controller is optional
Extension | Support maximum 8 pcs PCI-E Gen3
Monitoring Management | Motherboard Integrated BMC module ，supporting IPMI2.0、SNMP v3 and KVM over IP， Disk status LED display
Case Dimensions | 4U，standard rack type 176mm x 432mm x 886mm

## Slide 7
Introduction of Product Module Tray
Chassis front panel
Front hard disk tray
Mainboard tray
Top cover of chassis
Hard disk tray top cover
Rear hard disk tray

## Slide 8
Introduction of Mainboard
Central chassis fan 2. CPU heat sink 3. Memory slot 4. wind scooper 5. Right I/O extension module 6. Left I/O extension module 7. Right Riser module 8. Redundant power supply

## Slide 9
Contents
1
The Introduction of Storage Server Market
2
Introduction of S640-G20 product
3
Introduction of S640-G20 product features
4
Product competitive analysis of S640-G20
Notes: 先讲整个IT行业的大背景

## Slide 10
S650G20 Product Features
3
1
5
4
2
S650G20
Low CTO
High Reliability
Mass Storage
Capacity
Manageability
High Performance

## Slide 11
Compatible with the latest 6 TB hard disk, providing mass storage capacity
36
×
Single system storage capacity maximum 216 TB!!!!!!

## Slide 12
Upgraded Architecture making the system performance improve
High performance
12Gb/s SAS Technology
Haswell Processor Architecture
PCIe 3.0
DDR4 Memory Technology

## Slide 13
Star light diagnosis, easy to maintain
The machine with a total of 60 monitoring signals, including the comprehensive monitoring for CPU, memory, Riser expansion card, the power signal,，every part of the system in-place, working state.

## Slide 14
Rich management functions,
performance optimization, one-click seting
BMC support SD card equipment log storage, and can save system information unlimited
set the optimal configuration of
Benchmark test on one click
  Sugon R&D management module（BMC）independent，support IPMI2.0 ， SNMP，Independent management port ，support SOL,CLI,KVM over IP，Support remote upgrade BIOS/Firmware
  BMC can realize the monitoring on parts consumption and limit the machine power consumption;
  Can remote update a BIOS FW By BMC Web that’s a convenient and humanistic upgrade strategy
  The first time implementation monitoring of card key information by BMC ， contains the manufacturer, type, speed, link state, MAC address,and the correspondence between the MAC and NIC；
BMC monitoring

## Slide 15
Platinum CRPS power supply，Green energy-saving
Power DIP Board, with no cable routing, seems more artistic and better cooling effect
Support power cold backup：
Incold standby mode, the power conversion efficiency can be increased 3% again, up to 95%.
Multiple contact sensors：
The machine system containing 25 sensors to ensure the machine heat noise effect balanced
CRPS Power Supply

## Slide 16
Provide custom services at different
levels to meet customer demand
Simple logo
customization
Structure appearancecustomization
Solutions business customization
Function set
customization
Packaging, labels, BIOS and BMC interface logo
customization
According to the customer business characteristics，customize by the solution of binding the customer application with Sugon hard and soft product to improve the TCO of system.
According to user requirements and combining with Sugon product to customize, including product specifications, the server internal structure, product appearance.
Require to customize management functions for customer on BMC management chip, the BIOS etc.
复杂
简单
Simple
Complex

## Slide 17
Contents
1
The Introduction of Storage Server Market
2
Introduction of S640-G20 product
3
Introduction of S640-G20 product features
4
Product competitive analysis of S640-G20
Notes: 先讲整个IT行业的大背景

## Slide 18
Competition analysis：SMC Storage Server
Product mode | SugonS640-G20 | SMC 24/36
CPU | dualE5-2600 v3 | dualE5-2600 v3
Memory | 24 pcs DDR4 2133/ 1866 ECC memory | 8/24 slotDDR4
Height | 4U | 4U
Store Controller | 12G SAS and SAS RAID | 12G SAS and SAS RAID
2.5 inch hard disk | 4 | 2
The number of 3.5 -inch hard disk | 24/36（6TB） | 24/36
The integrated network port | 2x1GbE | 2x1Gb
PCI-Eextension | 8 pcs PCI-E Gen3 | 4 pcs PCI-E Gen3
Case Dimensions (mm) | 176 x 432 x 886 | 178 × 437 × 699
Other features | Support NVDIMM,PCI-E SSD | 
Sugon vs SMC
Product Advantage
Support rear 4 sets hotplug system disk.SMC only support 2 set
More PCIe slots.S640 - the G20 maximum 8 PCIe slots, can match more high-speed network card and IB card
Support NVDIMM.S640 - the G20 configurable NVDIMM to ensure that the memory data when the power outage.
Light diagnosis functionS640 - the G20 with more than 60 signal in system to monitor the state of CPU, memory, fan and other core components
Easy maintenance. S640 - the G20 support all travel guide.
SMC型号：
6048R-E1CR24N
6048R-E1CR36N
5048R-E1CR36L

## Slide 19
Competition analysis ：5288 V3
Product mode | SugonS640-G20 | Huawei5288 V3
CPU | dualE5-2600 v3 | dualE5-2600 v3
Memory | 24 pcs DDR4 2133/ 1866 ECC memory | 16 pcs DDR4
Height | 4U | 4U
Store Controller | 12G SAS and SAS RAID | 6Gb SAS and SAS RAID
2.5 inch hard disk | 4 | 4
The number of 3.5 -inch hard disk | 24/36（6TB） | 24/36
The integrated network port | 2x1GbE | 2x1GbE/4x1GbE
PCI-Eextension | 8 pcs PCI-E Gen3 | 6 pcs PCI-E X8 + 1个PCI-EX4
Case Dimensions (mm) | 176mm x 432mm x 886mm | 175 × 447 × 748
Sugon vs Huawei
Product Advantage
Larger memory capacity.S640-G20 support 24 DIMM slot, more than 5288v3
More PCIe S640-G20 support maximum eight PCIe slots, rear support only six
Support NVDIMM.S640 - the G20 configurable NVDIMM to ensure that the memory data when the power outage
Light diagnosis functionS640 - the G20 with more than 60 signal in system to monitor the state of CPU, memory, fan and other core components

## Slide 20
Competition analysis ：
Product mode | SugonS640-G20 | InspurSA5224L2
CPU | Dual E5-2600 v3 | SingleE3-1200
Memory | 24 pcs DDR4 2133/ 1866 ECC内存 | 4 pcs DDR3
Height | 4U | 4U
Store Controller | 12G SAS and SAS RAID | 6G SAS and SAS RAID
2.5 inch hard disk | 4 | 2
The number of 3.5 -inch hard disk | 24/36（6TB） | 24
The integrated network port | 2x1GbE | 2x1Gb
PCI-Eextension | 8个PCI-E Gen3 | 4个PCI-E Gen3
Case Dimensions (mm) | 176x 432 x 88 | 178 × 437 × 699
Other features | Support NVDIMM,PCI-E SSD | 
Sugon vs Inspur
Product Advantage
Higher CPU performance. The latter is single way server products
Support rear four sets hotplug system disk。The latter only supports two system disk
More PCIe slots.S640 - G20 maximum eight PCIe slots, can match more high-speed network card and IB card
BMCmanagement function. S640-the G20 adopted their own management module, ， the function supported more than Inspur/SMC storage server products
Light diagnosis functionS640 - the G20 with more than 60 signal in system to monitor the state of CPU, memory, fan and other core components
All Inspur24/36 disk storage server OEM SMC product！！！

## Slide 21
Competition analysis ：HP SL4500
Product mode | SugonS640-G20 | HP SL4500
CPU | Dual E5-2600 v3 | Dual E5-2400 v2
Memory | 24 pcs DDR4 2133/ 1866 ECC内存 | 12 pcs DDR2 1033 ECC内存
Height | 4U | 4.3U
Store Controller | 12G SAS和SAS RAID | 6Gb SAS和 SAS RAID
2.5 inch hard disk | 4 | 6
The number of 3.5 -inch hard disk | 24/36（6TB） | 60（4TB）
The integrated network port | 2x1GbE | 2x1GbE + 2x10GbE
PCI-Eextension | 8 pcs PCI-E Gen3 | 1 pcs PCI-E x8
Case Dimensions (mm) | 176 x 432 x 886 | 189 x 443 x 890
Othe | Support NVDIMM,PCI-E SSD | 可扩展为2-3节点
Sugon vs HP
Product Advantage
Higher CPU performance. The latter is the last generation CPU architecture products
Larger memory capacity.Larger memory capacity.S640-G20 support 24 DIMM slot, more than SL4500
More PCIe slots.S640-G20 maximum eight PCIe slots, can match more high-speed network card and IB card
The system has high reliability。The latter power down in user ，system reliability is poor.
Light diagnosis function.S640 - the G20 with more than 60 signal in system to monitor the state of CPU, memory, fan and other core components